74LS107

        Function Table s(107/107a)

 Logic Diagram (107a)

Description:
The ‘107 contain two independent J-K flip-flops with
individual J-K, clock, and direct clear inputs. The ‘107
is a positive pulse-triggered flip-flop. The J-K input data
is loaded into the master while the clock is high and
transferred to the slave and the outputs on the high-to-
low clock transition. For these devices the J and K inputs
must be stable while the clock is high.

The “LS107A contain two independent negative-edge-
triggered flip-flops. The J and K inputs must be stable
prior to the high-to-low clock transition for predictable
operation. When the clear is low, it overrides the clock
and data inputs forcing the Q output low and the !Q
output high.

Function Table (107a)
Inputs					Outputs
!CLR	CLK	J	K		Q	!Q
L	X	X	X		L	H
H	Rising Edge	L	L		Q0	!QO
H	Rising Edge	H	L		H	L
H	Rising Edge	L	H		L	H
H	Rising Edge	H	H		TOGGLE

Function Table (107)
Inputs					Outputs
!CLR	CLK	J	K		Q	!Q
L	X	X	X		L	H
H	Falling Edge	L	L		Q0	!QO
H	FallingEdge	H	L		H	L
H	Falling Edge	L	H		L	H
H	Falling Edge	H	H		TOGGLE